FRINGE CORRECTION OF I BAND IMAGES

	This will be a brief desciption of the fringe correction process for
I band images.  I will explain what the fringe correction is and how we 
go about the correction.
	Fringes occur on I band images because of light being emitted from
the atmosphere at wavelenghts corresponding to the I band filter.  This
emission can change in intensity throughout the night and fringes will in
general be located in differing locals of the ccd from night to night.  
	It is possible to make a map of these fringes for a given night.  One
needs to have enough I band images throughout the course of the night to 
construct a sky flat.  One also needs a good I dome flat for the night.  
	In iraf construct both your dome and sky flats.  Then flat correct your
sky flat with your dome flat, using the ccdproc program in imred.ccdred.  
This will produce a field primarily of fringes, but there remains a slight
background surface and a background sky level.  In order to remove this, use 
the iraf procedure mkfringe in the imred.ccdred package.  Enter the name of 
your fringe image, along with the name for the final resulting image.  
Mkfringe subtracts the background surface, giving you a fringe image with a 
mean around zero but with a high sigma because of the fringes.
	Those same steps can be carried out in idl if you would rather not 
venture into iraf.  However, at this time the idl routine which I wrote to 
subtract off the fringe patern only accepts iraf images.  So it will need to
be changed if your images are not iraf images.  Remeber to flatfield your
images before doing the fringe correction.  Use the dome flat for flatfielding.
	Once you have created your fringe image, you are ready to perform the
fringe subtraction.  This is done in IDL.  Iraf has its own program to do this
but it is not as exacting as ours.  The fringe pattern will tend to change in
intesity thoughout the night.  You will want to scale your fringe image so as
to minimize the noise in your cleaned image.  The iraf program does not do 
this.
	There are certain parameters to set in the idl program before running
it.  The program has a driver program called fringedrive.pro.  The input to 
this program is a list of iraf image file names.  In fringedrive you will need
to set the image directory.  This is in the second line of the program.  The
next thing to set is the name of the fringe image.  The variable is called 
fringe, and you just give it the name of your iraf .imh fringe image.  However,
you do not include the .imh in the name of the image.  Once this is done you
are set to run the program.  Fringedrive calls a second routine called 
fringcor.  This is where the actuall searching of minimum signal to noise 
occurs.
	The output of the program is a fits file containing the fringe 
corrected image.  So while it reads in an iraf file, a fits file is produced.
The resulting image will be sent to the same directory as you .imh images, and
it will have the suffix, FRINGCOR.
	The fringe program will also display a graph of the minimum of 
noise as you vary the scale factor of the fringe image.  You will have 
the option of printing this graph.  Just answer y or n.
	 You are now ready to surface your cleaned fits image and then load it 
on to the data base.  
	So that is the basics behind the fringe correction of images.  There
is room for improvement, and this basic routine can be modified to be 
incorporated in existing idl cleaning routines.

Cheers,
Jason